## Slide 1: http://www.comp.nus.edu.sg/~cs2100/
Lecture #14
Logic Circuits

## Slide 2: Lecture #14: Logic Circuits
Logic Gates
  1.1 Inverter/AND/OR Gates
  1.2 NAND/NOR Gates
  1.3 XOR/XNOR Gates
Logic Circuits
  2.1 Drawing and Analysing Logic Circuits
Universal Gates
  3.1 NAND Gate
  3.2 NOR Gate
  3.3 SOP and NAND Circuits
  3.4 POS and NOR Circuits
Integrated Circuit (IC) Chip
Programmable Logic Array
Read Only Memory (ROM)

## Slide 3: 1. Logic Gates
Gate symbols
a
b
ab
a
b
a+b
a
a'
a
b
(a+b)'
a
b
(ab)'
a
b
a  b
a
b
ab
&
a
b
a+b
1
a
a'
1
a
b
(ab)'
&
a
b
(a+b)'
1
a
b
a  b
=1
EXCLUSIVE OR
AND
OR
NOT
NAND
NOR
Symbol set 1
Symbol set 2
(ANSI/IEEE Standard 91-1984)

## Slide 4: 1.1 Inverter/AND/OR Gates
Inverter (NOT gate)
A
A'
A
A'
A | A'
0 | 1
1 | 0
AND gate
A
B
A  B
A | B | A  B
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
OR gate
A
B
A+B
A | B | A + B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 5: 1.2 NAND/NOR Gates
NAND gate
A | B | (A  B)'
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
A
B
(A  B)'
A
B
(A  B)'

NAND
Negative-OR

NOR gate

A
B
(A + B)'
A
B
(A + B)'
A | B | (A + B)'
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
NOR
Negative-AND



## Slide 6: 1.3 XOR/XNOR Gates
XOR gate
A | B | A  B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
XNOR gate
A
B
A  B
A
B
(A  B)'
A | B | (A  B)'
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
XNOR can be represented by  (Example: A  B)


## Slide 7: 2. Logic Circuits (1/2)
Fan-in: the number of inputs of a gate.
Gates may have fan-in more than 2.
  Example: a 3-input AND gate
Given a Boolean expression, we may implement it as a logic circuit.
Example: F1 = xyz' (note the use of a 3-input AND gate)
x
y
z
F1
z'
Every input must be connected in a working circuit!

## Slide 8: 2. Logic Circuits (2/2)
Example: F2 = x + y'z
Example: F3 = xy' + x'z
x
y'
z
F2
y'z
If complemented literals are available
If complemented literals are not available
x
z
F2
y'z
y
x'
z
F3
x'.z
x.y'
x
y'
z
F3
x'.z
x.y'
x
y
Draw a solid circle to denote that the wires intersect.

## Slide 9: 2.1 Analysing Logic Circuits

Given a logic circuit, we can analyse it to obtain the logic expression.
Example: Given the logic circuit below, what is the Boolean expression of F4?
A'B'
(A'B')+C
((A'B')+C)'
F4 = ((A'B')+C)' = (A+B)C'
F4
A
B
C
DLD page79 Quick Review Questions Questions 4-1 to 4-4.

## Slide 10: 3. Universal Gates
AND/OR/NOT gates are sufficient for building any Boolean function.
We call the set {AND, OR, NOT} a complete set of logic.
However, other gates are also used:
  Usefulness (eg: XOR gate for parity bit generation)
  Economical
  Self-sufficient (eg: NAND/NOR gates)

## Slide 11: 3.1 Universal Gates: NAND Gate
{NAND} is a complete set of logic.
Proof: Implement NOT/AND/OR using only NAND gates.
x
x'
(x∙x)' = x' (idempotency)
x
x∙y
y
(x∙y)'
((x∙y)'∙(x∙y)')' = ((x∙y)')' (idempotency)
= x∙y (involution)
x
x+y
y
x'
y'
((x∙x)'∙(y∙y)')' = (x'∙y')' (idempotency)
= (x')'+(y')' (DeMorgan)
= x+y (involution)

## Slide 12: 3.2 Universal Gates: NOR Gate
{NOR} is a complete set of logic.
Proof: Implement NOT/AND/OR using only NOR gates.
(x+x)' = x' (idempotency)
((x+y)'+(x+y)')' = ((x+y)')' (idempotency)
= x+y (involution)
((x+x)'+(y+y)')' = (x'+y')' (idempotency)
= (x')'∙(y')' (DeMorgan)
= x∙y (involution)
x
x'
x
x∙y
y
x'
y'
x
x+y
y
(x+y)'
DLD page79 Quick Review Questions Questions 4-6 to 4-8.

## Slide 13: 3.3 SOP and NAND Circuits (1/2)
An SOP expression can be easily implemented using
  2-level AND-OR circuit
  2-level NAND circuit
Example: F = AB + C'D + E
  Using 2-level AND-OR circuit
F
A
B
D
C
E

## Slide 14: 3.3 SOP and NAND Circuits (2/2)
Example: F = AB + C'D + E
  Using 2-level NAND circuit
F
A
B
D
C
E
F
A
B
D
C
E
F
A
B
D
C
E

## Slide 15: 3.4 POS and NOR Circuits (1/2)
A POS expression can be easily implemented using
  2-level OR-AND circuit
  2-level NOR circuit
Example: G = (A+B)  (C'+D)  E
  Using 2-level OR-AND circuit
G
A
B
D
C
E

## Slide 16: 3.4 POS and NOR Circuits (2/2)
Example: G = (A+B)  (C'+D)  E
  Using 2-level NOR circuit
G
A
B
D
C
E
G
A
B
D
C
E
G
A
B
D
C
E

## Slide 17: Reading
Propagation Delay
  Read up DLD section 4.5, pg 75 – 77.
Integrated Circuit Logic Families
  Read up DLD section 4.6, pg 77 – 78.

## Slide 18: 4. Integrated Circuit (IC) Chip
Example of a 74LS00 chip: Quad NAND gates.
1
2
3
4
5
6
7
14
13
12
11
10
9
8
GND
Vcc = 5v

## Slide 19: 5. Programming Logic Array (PLA) (1/3)
A programmable integrated circuit – implements sum-of-products circuits (allow multiple outputs).
2 stages
  AND gates = product terms
  OR gates = outputs
Connections between inputs and the planes can be ‘burned’.
AND gates
Inputs
Outputs
OR gates
Product terms

## Slide 20: 5. PLA Example (2/3)

## Slide 21: 5. PLA Example (3/3)
Simplified representation of previous PLA.
Inputs
Outputs
AND plane
OR plane
A'B'C
A'BC'
A
B
C
A
B
C
D
E
F

## Slide 22: 6. Read Only Memory (ROM)
Similar to PLA
  Set of inputs (called addresses)
  Set of outputs
  Programmable mapping between inputs and outputs
Fully decoded: able to implement any mapping.
In contrast, PLAs may not be able to implement a given mapping due to not having enough minterms.

## Slide 23: Lab Assignments (1/2)
For the next few labs, you will implement simple circuits using the Logic Trainer

## Slide 24: Lab Assignments (2/2)
Lab sheets will be given out in lectures.
Remember to read the Logic Lab Guidelines before you come for your first lab session.
Please read the lab sheet and fill up as much as you can before the lab, or you may not have enough time to complete your lab experiment.
Aim to finish your experiment as quickly as possible. Vacate the room 10 minutes before the hour. If not, just submit your lab report.

## Slide 25: End of File