## Slide 1: http://www.comp.nus.edu.sg/~cs2100/
Lecture #3a
Data Representation and Number Systems

## Slide 2: Questions?
Scan and ask your questions here! (May be obscured in some slides)
Ask at https://sets.netlify.app/module/66988ae3322ba68d1103fdd4
OR

## Slide 3: Lecture #3: Data Representation and Number Systems (1/2)
Data Representation
Decimal (base 10) Number System
Other Number Systems
Base-R to Decimal Conversion
Decimal to Binary Conversion
  5.1 Repeated Division-by-2
  5.2 Repeated Multiplication-by-2
Conversion Between Decimal and Other Bases
Conversion Between Bases
Binary to Octal/Hexadecimal Conversion

## Slide 4: Lecture #3: Data Representation and Number Systems (2/2)
ASCII Code
Negative Numbers
  10.1 Sign-and-Magnitude
  10.2 1s Complement
  10.3 2s Complement
  10.4 Comparisons
  10.5 Complement on Fractions
  10.6 2s Complement Addition/Subtraction
  10.7 1s Complement Addition/Subtraction
  10.8 Excess Representation
Real Numbers
  11.1 Fixed-Point Representation
  11.2 Floating-Point Representation

## Slide 5
1. Data Representation (1/2)
Basic data types in C:
int
float
double
char
Variants: short, long
How data is represented depends on its type:
01000110
As an ‘int’, it is 70
As a ‘char’, it is ‘F’
11000000110100000000000000000000
As an ‘int’, it is -1060110336
As an ‘float’, it is -6.5

## Slide 6
1. Data Representation (2/2)
Data are internally represented as sequence of bits (binary digits). A bit is either 0 or 1.
Other units
  Byte: 8 bits
  Nibble: 4 bits (rarely used now)
  Word: Multiple of bytes (eg: 1 byte, 2 bytes, 4 bytes, etc.) depending on the computer architecture
N bits can represent up to 2N values
  Eg: 2 bits represent up to 4 values (00, 01, 10, 11); 4 bits represent up to 16 values (0000, 0001, 0010, …., 1111)
To represent M values, log2M bits required
  Eg: 32 values require 5 bits; 1000 values require 10 bits

## Slide 7
2. Decimal (base 10) Number System
A weighted-positional number system.
Base (also called radix) is 10
Symbols/digits = { 0, 1, 2, 3, 4, 5, 6, 7, 8, 9 }
Each position has a weight of power of 10
  Eg: (7594.36)10 = (7 × 103) + (5 × 102) + (9 × 101) + (4 × 100) + (3 × 10-1) + (6 × 10-2)
(anan-1… a0 . f1f2 … fm)10 = (an x 10n) + (an-1x10n-1) + … + (a0 x 100) + (f1 x 10-1) + (f2 x 10-2) + … + (fm x 10-m)

## Slide 8
3. Other Number Systems (1/2)
Binary (base 2)
  Weights in powers of 2
  Binary digits (bits): 0, 1
Octal (base 8)
  Weights in powers of 8
  Octal digits: 0, 1, 2, 3, 4, 5, 6, 7.
Hexadecimal (base 16)
  Weights in powers of 16
  Hexadecimal digits: 0, 1, 2, 3, 4, 5, 6, 7, 8, 9, A, B, C, D, E, F.
Base/radix R:
  Weights in powers of R

## Slide 9
3. Other Number Systems (2/2)
In some programming languages/software, special notations are used to represent numbers in certain bases
  In programming language C
    Prefix 0 for octal. Eg: 032 represents the octal number (32)8
    Prefix 0x for hexadecimal. Eg: 0x32 represents the hexadecimal number (32)16
  In QTSpim (a MIPS simulator you will use)
    Prefix 0x for hexadecimal. Eg: 0x100 represents the hexadecimal number (100)16
  In Verilog, the following values are the same
    8’b11110000: an 8-bit binary value 11110000
    8’hF0: an 8-bit binary value represented in hexadecimal F0
    8’d240: an 8-bit binary value represented in decimal 240

## Slide 10
4. Base-R to Decimal Conversion
Easy!
  1101.1012 = 123 + 122 + 120 + 12-1 + 12-3
= 8 + 4 + 1 + 0.5 + 0.125 = 13.62510
  572.68 =
  2A.816 =
582 + 781 + 280 + 68-1
= 320 + 56 + 2 + 0.75 = 378.7510
  341.245 =
2161 + 10160 + 816-1
= 32 + 10 + 0.5 = 42.510
352 + 451 + 150 + 25-1 + 45-2
= 75 + 20 + 1 + 0.4 + 0.16 = 96.5610

DLD page 42 Quick Review Questions Questions 2-1 to 2-4.

## Slide 11
5. Decimal to Binary Conversion
For whole numbers
  Repeated Division-by-2 Method
For fractions
  Repeated Multiplication-by-2 Method

## Slide 12
5.1 Repeated Divison-by-2
To convert a whole number to binary, use successive division by 2 until the quotient is 0. The remainders form the answer, with the first remainder as the least significant bit (LSB) and the last as the most significant bit (MSB).
(43)10 = ( ? )2
101011

## Slide 13
5.2 Repeated Multiplication-by-2
To convert decimal fractions to binary, repeated multiplication by 2 is used, until the fractional product is 0 (or until the desired number of decimal places). The carried digits, or carries, produce the answer, with the first carry as the MSB, and the last as the LSB.
(0.3125)10 = ( ? )2
.0101

## Slide 14
6. Conversion Between Decimal and Other Bases
Base-R to decimal: multiply digits with their corresponding weights
Decimal to binary (base 2)
  Whole numbers: repeated division-by-2
  Fractions: repeated multiplication-by-2
Decimal to base-R
  Whole numbers: repeated division-by-R
  Fractions: repeated multiplication-by-R
DLD page 42 Quick Review Questions Questions 2-5 to 2-8.

## Slide 15
7. Conversion Between Bases
In general, conversion between bases can be done via decimal:
Shortcuts for conversion between bases 2, 4, 8, 16 (see next slide)
Base-2 Base-2
Base-3 Base-3
Base-4 Decimal Base-4
… ….
Base-R Base-R

## Slide 16
8. Binary to Octal/Hexadecimal Conversion
Binary  Octal: partition in groups of 3
  (10 111 011 001 . 101 110)2 =
Octal  Binary: reverse
  (2731.56)8 =
Binary  Hexadecimal: partition in groups of 4
  (101 1101 1001 . 1011 1000)2 =
Hexadecimal  Binary: reverse
  (5D9.B8)16 =

(2731.56)8
(10 111 011 001 . 101 110)2
(5D9.B8)16
(101 1101 1001 . 1011 1000)2
DLD page 42 Quick Review Questions Questions 2-9 to 2-10.

## Slide 17: Quiz
Please complete the “CS2100 C Number Systems Quiz 1” in Canvas.
  Access via the “Quizzes” tool in the left toolbar and select the quiz on the right side of the screen.

## Slide 18: End of File